## Slide 1: Basic structure of Computer Architecture

## Slide 2
Outline
  Computer Architecture
  Hardware, Software, Firmware
  Block Diagram of Computer Architecture
  How does instruction execute in Computer System?

## Slide 3
Computer Architecture is the interface between software and hardware. It is what the programmer sees.
A computer system is sometimes subdivided into two functional entities: hardware and software.
The hardware of the computer consists all the electronics components and electromechanical devices that comprise the physical entity of the device.
Computer software consists of the instructions and data that the computer manipulates to perform various data-processing tasks.
Firmware falls between hardware and software. Firmware consists of programs that are included into electronic circuits during their manufacture. Firmware is used when the programs must be retained in case of power failure and when programs are not expected to be changed.

## Slide 4
Computer Architecture refers to those attributes of a system that have a direct impact on the logical execution of a program. Examples:
  the instruction set
  the number of bits used to represent various data types
  I/O mechanisms
  memory addressing techniques

## Slide 5
Computer Organization refers to the operational units and their interconnections that realize the architecture specifications. Examples are things that are transparent to the programmer:
  control signals
  interfaces between computer and peripherals
  the memory technology being used

## Slide 6
Input
Memory
Output
Control
Arithmetic Logic Unit (ALU)
Data/Instruction
Control
Block Diagram of Computer Architecture

## Slide 7
To execute instructions computer performs the following steps:
  The control unit reads or fetches an instruction from memory and decodes or translates it.
  For arithmetic or logic-type instructions, the control units generates enable signals for the ALU to perform the required operations.
  For input/output (I/O) instructions, the control unit generates enable signals for the I/O either to input data from or output data to external devices.